## Slide 1: Developing a quality system: finding your place on the quality ladder
Graham H Beastall
gbeastall@googlemail.com

## Slide 2: Outline of talk
What is quality in laboratory medicine?
The quality ladder
Why does quality matter?

## Slide 3: Definition of quality
Dictionary:
  ‘Degree or grade of excellence’
International Standards Organisation (ISO 9000)
  ‘Degree to which a set of inherent characteristics fulfils requirements’

## Slide 4: Different perceptions of a quality test
Manufacturer “CE marked”
Lab director “allows us to maintain accreditation”
Lab manager “inexpensive, requires unskilled staff”
Technologist “never fails IQC”
Lab consultant “high clinical sensitivity & specificity”
A&E physician “available at the bedside - whole blood”
Paediatrician “requires very small sample volume”
Patient “gives a quick answer / clear result”
Adapted from Callum Fraser 2001

## Slide 5: Quality in different settings
Blood glucose measurement in same patient
Technologist in laboratory
Nurse in diabetic clinic
Diabetic patient in own home
Current requirements for quality standards
ISO 15189
No Standard
ISO 22870

## Slide 6: How much quality?
%Quality
100
Perfection - target?
Highest - practice
Minimum - defined
Median - practice
A
B
C
Substandard
Adequate
Good
Aspiration?
Continuous quality improvement

## Slide 7: Resourcing quality
Resource
Quality
Direct relationship between resource
applied and quality of product
Additional quality possible
but greater resource required
Little gain in quality despite
considerable extra resource

## Slide 8: Assuring quality in every laboratory
Availability
Appropriateness
Accuracy
Reproducibility
Timeliness
Clinical advice
Governance
Cost effectiveness
Professional staff
Environment
Organisation
Equipment
Records
Audit
Development
Training / CPD
Quality management
QUALITY
Patient/user
satisfaction
The responsibility
of everyone !

## Slide 9: Outline of talk
What is quality in laboratory medicine?
The quality ladder
Why does quality matter?

## Slide 10: Laboratory medicine: the total testing process (TTP)
Patient
Need for laboratory medicine
4a
Pre-analytical
4b Analytical
4c
Post-analytical
Doctor
Laboratory
medicine
phases
1
2
3
5
6

## Slide 11: Laboratory medicine: three phases
Pre-analytical
Analytical
Post analytical
Test selection
Specimen collection
Specimen transport
Specimen reception
46-68% Lab errors*
Specimen processing
Analysis
Quality control
Result validation
Data into knowledge
Clinical reporting
Clinical liaison
Clinical follow-up
<10% Lab errors
18-47% Lab errors*
* Plebani M. Clin Chem Lab Med 2006; 44: 750-9

## Slide 12: Laboratory medicine: quality ladder

## Slide 13: Laboratory medicine: quality ladder -1
1. Analytical quality

## Slide 14: Analytical quality: stages
Analytical
IQC
Internal quality control
Variability, imprecision
EQA
External quality assessment
Accuracy, trueness
Action limits
Determine acceptability of analytical data
Analytical goals
Are assays fit for clinical purpose?

## Slide 15: Analytical quality: laboratory support
Analytical
IQC
Internal quality control
Variability, imprecision
EQA
External quality assessment
Accuracy, trueness
Action limits
Determine acceptability of analytical data
Analytical goals
Are assays fit for clinical purpose?
Daily
monitoring
Formal
review
Audit
Target
setting

## Slide 16: Analytical quality: what can go wrong?
Analytical
IQC
Internal quality control
Variability, imprecision
EQA
External quality assessment
Accuracy, trueness
Action limits
Determine acceptability of analytical data
Analytical goals
Are assays fit for clinical purpose?
Result can’t be repeated
Inaccurate
result
Wrong decision.
Patient safety issue
Assay not fit for purpose

## Slide 17: Laboratory medicine: quality ladder - 2
1. Analytical quality
2. Pre-analytical quality

## Slide 18: Pre-analytical phase: stages
Pre-analytical
phase
Test selection
Right test, right patient, answer clinical question.
Clear on request form
Sample collection
Right sample, right time, right tube, right collection.
Clear on request form
Sample transport
Priority status, timing, temperature, special requirements
Sample receipt
Booking, processing, schedule for analysis, storage, disposal
Steps before the sample reaches the lab: ‘pre-pre-analytical’: most errors

## Slide 19: Pre-analytical phase: laboratory support
Pre-analytical
phase
Test selection
Right test, right patient, answer clinical question.
Clear on request form
Sample collection
Right sample, right time, right tube, right collection.
Clear on request form
Sample transport
Priority status, timing, temperature, special requirements
Sample receipt
Booking, processing, schedule for analysis, storage, disposal
Discussion with users
Regular audit & feedback
Instructions and guidance
Educational
support

## Slide 20: Pre-analytical phase: what can go wrong?
Pre-analytical
phase
Test selection
Right test, right patient, answer clinical question.
Clear on request form
Sample collection
Right sample, right time, right tube, right collection.
Clear on request form
Sample transport
Priority status, timing, temperature, special requirements
Sample receipt
Booking, processing, schedule for analysis, storage, disposal
Wrong outcome. Patient safety issue
Specimen compromised
Inappropriate investigation
Incorrect
specimen

## Slide 21: Laboratory medicine: quality ladder - 3
3. Post-analytical quality
1. Analytical quality
2. Pre-analytical quality

## Slide 22: Post-analytical phase: stages
Post-analytical
phase
Follow-up
Treatment, further tests, referral, discharge
Reporting
Auto / manual report with comments as appropriate
Critical values
Proactive reporting outside agreed limits
Steps after the report leaves the lab: ‘post-post-analytical’: most errors
Test validation
Meets reporting criteria
Interpretation
Reference intervals
Link to clinical question
Report receipt
Report accessed within
appropriate time frame

## Slide 23: Post-analytical phase: laboratory support
Post-analytical
phase
Follow-up
Treatment, further tests, referral, discharge
Reporting
Auto / manual report with comments as appropriate
Critical values
Proactive reporting outside agreed limits
Report receipt
Report accessed within appropriate time frame
Steps after the report leaves the lab: ‘post-post-analytical’: most errors
Test validation
Meets reporting criteria
Interpretation
Reference intervals. Link to clinical question
Clinical
audit
Educational support
Discussion with users
Guidance and advice

## Slide 24: Post-analytical phase: what can go wrong?
Post-analytical
phase
Follow-up
Treatment, further tests, referral, discharge
Reporting
Auto / manual report with comments as appropriate
Critical values
Proactive reporting outside agreed limits
Report receipt
Report accessed within appropriate time frame
Steps after the report leaves the lab: ‘post-post-analytical’: most errors
Test validation
Meets reporting criteria
Interpretation
Reference intervals. Link to clinical question
Wrong action. Patient safety issue
Incorrect interpretation
Invalid
result
Vital result overlooked

## Slide 25: Laboratory medicine: quality ladder - 4
3. Post-analytical quality
1. Analytical quality
4. Quality management /
lab accreditation
2. Pre-analytical quality

## Slide 26: Laboratory medicine: tying the TTP together
Patient
Need for laboratory medicine
Pre-analytical
Analytical
Post-analytical
Doctor
4 Laboratory
medicine
phases
1
2
3
5
6
Quality management / laboratory accreditation

## Slide 27: Where is your laboratory on the: quality ladder?
3. Post-analytical quality
1. Analytical quality
4. Quality management /
lab accreditation
2. Pre-analytical quality

## Slide 28
Developing quality competence in the medical laboratory (DQCML): outline
Education & Management Division (EMD)

## Slide 29: Laboratory medicine: the quality ladder
Internal quality control
External quality assessment
Local liaison
International liaison
Accreditation preparation
Quality management system
Accreditation
individual lab
application

## Slide 30: DQCML: the full programme
Internal quality control
External quality assessment
Local liaison
International liaison
Accreditation preparation
Quality management system
Accreditation
individual lab
application
Rest of world
ISO 15189
Visiting lecturer programme
Distance learning
Africa
SLMTA/SLIPTA
Analytical quality
Lab management
Mentoring lab director
EB to facilitate
WHO, ASLM, Other
EB to facilitate
ILAC, WHO, Other
C-AQ + nat society
C-CLM + region
‘One to one’ support

## Slide 31: Outline of talk
What is quality in laboratory medicine?
The quality ladder
Why does quality matter?

## Slide 32: Patient safety
First rule of medicine: ‘Do no harm’
Poor quality laboratory medicine can harm patients:
  Missed or delayed diagnosis / treatment
  Incorrect diagnosis / treatment
  Unforseen clinical events
    Side effects, morbidity, even death

## Slide 33: Alan Wu publications
www.alanhbwu.com

## Slide 34: Laboratory input to clinical effectiveness
Lab Input
Direct patient care (medical doctors)
Reflective testing
Interpretive comments
cumulative reports
Critical result reporting
Clinical advisory service
Multidisciplinary team participation
Clinical audit
leadership
Clinical practice guideline implementation
Successful input is predicated on a high quality laboratory service

## Slide 35: Laboratory quality and governance
Hospital / employer governance structure
Laboratory quality policy & quality objectives
Laboratory quality reports
Laboratory quality standards
Evidence of meeting quality standards
Marketing laboratory services

## Slide 36: Quality and laboratory reputation
As laboratory quality improves, reputation grows
leading to a ‘basket full’ of opportunity
Laboratory quality
User satisfaction
New customers
Clinical trials
Research collaboration